## Slide 1
Why a Swarm?
Object Manipulation and Position Control Using a Swarm With Global Inputs
Shiva Shahrokhi and Aaron T. Becker
sshahrokhi2@uh.edu atbecker@uh.edu .
Object Manipulation
Rules: Inputs are simple & global. All robots receive exactly the same commands: move toward brightest light
Goal: Position and orientation (pose) control of the pink object using the swarm force and torque
Simulation of robots exerting torque on a hinged “door”
Simulation of swarm orientation manipulation
(c) 97 hardware robots applying torque to an object
Four Challenges With Increasing Complexity
Swarm robots:
Can pass through constrictions
Can bend around obstacles
Can be simple:
  Easy to design, build, test
  Disposable/ replaceable
  Small, tiny, nano/micro robots
#1: Swarm torque control on pivoted object
Grand Challenge: Pose Control
YouTube channel
Website, C.V.
#3: Straight translation while regulating
object orientation
Swarm Piano Mover’s video
#2: Orientation control of the object
#4: Line following with perpendicular orientation
a) Pushing an object perpendicular to its minor axis, the swarm spreads around the object
b) Applying force perpendicular to the object's long axis reduces the probability of splitting the swarm
Manipulating the object to the desired pose(orientation and position)
Experiment With Hardware Robots
Pure torque control experiments with kilobots
Kilobots are programmed to go toward the brightest light in the room as their global input
Actual Size