## Slide 1
Why a Swarm?
Object Manipulation and Position Control Using a Swarm With Global Inputs
Shiva Shahrokhi, Aaron T. Becker
sshahrokhi2@uh.edu, atbecker@uh.edu .
Object Manipulation
Rules: Inputs are simple & global: all robots receive exactly the same commands
Goal: Pose Control of the pink object using the swarm force and torque
Challenges
Swarm robots:
Can pass through constrictions
Can bend around obstacles
Can be simple:
  Easy to design, build, test
  Disposable/ replaceable
  Small, tiny, nano/micro robots
Torque Control of the object using swarm
Pose Control
YouTube channel
Website, C.V.
(3) Straight Translation While Regulating
Object Orientation
Swarm Piano Mover’s video
Department of Electrical and Computer Engineering,
University of Houston
(2)Orientation Control of the Object
(4) Line Following with perpendicular orientation
a.) Pushing an object perpendicular to its minor axis, the swarm spreads around the object
b.) Applying force perpendicular to the object's long axis reduces the probability of splitting the swarm
(5) Manipulating the object to the desired pose
Experiment With Hardware Robots
Pure Torque Control Experiments With Kilobots
Kilobots are programmed to go toward the brightest light in the room as their global input