## Slide 1
Why Covariance Control?
Shaping a Swarm Using Wall Friction and a Shared Control Input
Shiva Shahrokhi, Aaron T. Becker
sshahrokhi2@uh.edu, atbecker@uh.edu
Using Friction to Break Symmetry
Position Control using Wall Friction
Multi Robot Control
Vascular networks are common in biology
Shared inputs means each member of
the swarm receives the same control
input
Navigating a swarm using shared
inputs is challenging due to obstacles
and symmetry
Results
YouTube channel
Website, C.V.
Department of Electrical and Computer Engineering,
University of Houston
We designed an algorithm for controlling the position of two robots
For simplicity, we assume that friction
is infinite
Following this path we can get to the ending points when getting the same input.
Two robot positioning: switching positions using walls with infinite friction
Maintaining group cohesion while steering a swarm through an arbitrary maze requires covariance control
Pushing swarm into vertical walls does not change x and y position correlation
We need to break this symmetry
Friction is sufficient to break the symmetry
Wall friction reduces forward force for robots near a wall, but not for free robots
We used kilobots to show that wall friction enables covariance control
Global Input: kilobots go to the brightest light source in the room
Plot shows covariance control is possible
Two robot positioning using hardware setup with two kilobot robots
Walls have nearly infinite friction
Robot with blue path is stopped by the wall until the light changes orientation
The orange robot in free-space is unhindered
Future Opportunities
Robot
Bottom Path
Top Path
Goal Positions
We can extend this algorithm to control the position of n robots
Algorithm has n iterations
Iteration k assumes k-1 robots are at goal positions and moves kth robot to desired position
Efficiently steer robot swarm through a maze
Use obstacles and wall friction to partition swarm
Implementing n robot position algorithm with kilobots
Solving position control algorithm with finite friction
Automatic covariance control law using wall friction